5090209351 杜溪

Task 1
(a)TCP/FTP
(b)

0.2	0.4	0.6	0.8	1
tcp: 389660 / cbr: 107000 / total: 496660 / tcp ratio: 0.7846 / cbr ratio: 0.2154	tcp: 308040 / cbr: 226000 / total: 534040 / tcp ratio: 0.5768 / cbr ratio: 0.4232	tcp: 183300 / cbr: 342500 / total: 525800 / tcp ratio: 0.3486 / cbr ratio: 0.6514	tcp: 183300 / cbr: 405000 / total: 588300 / tcp ratio: 0.3116 / cbr ratio: 0.6884	tcp: 9280 / cbr: 586500 / total: 595780 / tcp ratio: 0.0156 / cbr ratio: 0.9844

TCP uses more bandwidth at first, but UDP gradually uses more bandwidth as its	sending rate increases and its traffic dominates the bottleneck at 1Mbps. The UDP traffic is	favored because it has no flow control.
(c)
tcp: 9280
cbr flow 1: 478500
cbr flow 2: 108000
total: 595780
tcp ratio: 0.0156
cbr flow 1 ratio: 0.8031
cbr flow 2 ratio: 0.1813
The UDP/CBR flow generated by node 2 is favored because it's sent at a higher rate.
(d)
10ms	15ms	20ms	25ms	30ms	35ms	40ms
tcp1: 301880 / tcp2: 247980 / total: 549860 / tcp1 ratio: 0.5490 / tcp2 ratio: 0.4510	tcp1: 272620 / tcp2: 261840 / total: 534460 / tcp1 ratio: 0.5101 / tcp2 ratio: 0.4899	tcp1: 300340 / tcp2: 231040 / total: 531380 / tcp1 ratio: 0.5652 / tcp2 ratio: 0.4348	tcp1: 247980 / tcp2: 264920 / total: 512900 / tcp1 ratio: 0.4835 / tcp2 ratio: 0.5165	tcp1: 280320 / tcp2: 229500 / total: 509820 / tcp1 ratio: 0.5498 / tcp2 ratio: 0.4502	tcp1: 264920 / tcp2: 224880 / total: 489800 / tcp1 ratio: 0.5409 / tcp2 ratio: 0.4591	tcp1: 280320 / tcp2: 184840 / total: 465160 / tcp1 ratio: 0.6026 / tcp2 ratio: 0.3974

The two connections both get approximately half of the bandwidth because of the	TCP flow control.

Task 2
(A)
1.Yes, some packets were dropped at node2 at about 5.5 sec.
2.(0.15+0.25-0.08)/0.08 = 4:1 (bandwidth of the 40ms-RTT flow vs. that of the	200ms-RTT one)
3.Because packets in the 200ms RTT TCP flow are more likely to time out, which	causes the flow control algorithm to decide to send at a lower rate.
4.By modifying the flow control algorithm to allow for a larger timeout.

(B)

1. The 4-connection application performs poorer than the single-connection one.
2. The 4-connection one takes about 40% of the bandwidth of Link 2-3.
3. It's not unfair.